## Slide 1: ENGI 301 Minimalist Wi-Fi LED Ticker Board Proposal
09.25.2023
Robert Heeter

## Slide 2: Background Information
In an age where messages and media are shared instantly and young adults spend hours before screens, retro-style low-resolution displays have caught my attention as a medium to stay connected and informed but not overwhelmed or distracted. The company Tidbyt (see https://tidbyt.com/products/tidbyt) makes an intriguing app-enabled display in this style, though with a high price. I plan to design a low-cost self-contained LED board (i.e. with a wood or acrylic housing) with WiFi, though I am still deciding the specific software functionality. Some ideas include:
A long-distance relationship message display board (I am currently in a long-distance relationship and this is a gift idea!), which retrieves messages sent via email or SMS text (see https://www.twilio.com/en-us/messaging and https://docs.python.org/3/library/smtplib.html).
A Spotify album artwork and currently-playing song display board using Spotify’s web API (see https://developer.spotify.com/documentation/web-api).
A current city weather display board with indoor temperature and humidity measurement using the National Weather Service’s API (see https://www.weather.gov/documentation/services-web-api).
A daily affirmation or rotating quote-of-the-day display board.

## Slide 3: System Block Diagram
Pocket Beagle
64x32 LED matrix
5V 4A power supply
DC power adapter
WiFi USB dongle
USB to micro USB adapter
WiFi micro USB breakout adapter
AHT10 temp/humidity sensor (?)
Push button (?)
USB1 bus
GPIO
SCL/SDA
I/O power
13 GPIO via IDC
Provided power cable

## Slide 4: Power Block Diagram
Pocket Beagle
64x32 LED matrix
5V 4A power supply
DC power adapter
WiFi USB dongle
USB to micro USB adapter
WiFi micro USB breakout adapter
AHT10 temp/humidity sensor (?)
Push button (?)
USB1 bus
5V/230mA
GPIO
5V/4A
3.3V
3.3V

## Slide 5: Components / Budget
Component | Need to Buy | Cost
64x32 3mm pitch RGB LED matrix (via Adafruit) | Yes* | $44.95
5V 4A switching power supply (Adafruit) | Yes | $14.95
WiFi USB dongle (Amazon) | Yes | $9.99
WiFi micro USB female breakout adapter (Adafruit) | Yes | $1.95 (÷2)
Male micro USB to female USB adapter (OEDK or Amazon) | Maybe | $0 or $5.59
Temperature and humidity sensor (Amazon) | Yes | $14.99 (÷10)
Female DC power adapter (2.1mm jack to screw terminal block) (OEDK or Adafruit) | Optional | $0 or 2.00
Push button (OEDK or Adafruit) | Optional* | $0 or $5.95
Acrylic or wood sheet housing material (OEDK or elsewhere) | Yes* | ?
Pocket Beagle, various wires and resistors, solder, etc. | No | N/A
* Indicates that I am willing to cover or contribute to the cost.